## Slide 1: Framework for Multidisciplinary Optimization
M Vishnu Sankar (18B030013)
Prof. Abhijit Gogulapati

## Slide 2: Contents
Why MDO?
Motivation, Goal and Deliverables
Framework Development
Framework Building-II
Framework Building-I
Challenges in FB-I
Framework Testing and Results
Conclusion & Future Work

## Slide 3: Why Optimization?
Notes: Deliverables
  A robust framework that's versatile to integrate any number of disciplines
  Communicate seamlessly with different analysis tools
  Predicts an optima or a set of optima which are better than baseline design
Problem Definition
  Theoretical structure for the seamless interfacing of different solvers/analysis tools
  Test it by actual implementation

## Slide 4: Traditional Approach
But why automation? Why is a framework necessary?
Notes: Deliverables
  A robust framework that's versatile to integrate any number of disciplines
  Communicate seamlessly with different analysis tools
  Predicts an optima or a set of optima which are better than baseline design
Problem Definition
  Theoretical structure for the seamless interfacing of different solvers/analysis tools
  Test it by actual implementation

## Slide 5: New Requirements – New Approach
"The Department of Defense (DoD) is seeking a concept of design (CoD) of an advanced aircraft configuration that provides at least 30% more aerodynamic efficiency than the Boeing 767 and Airbus A330 families of commercial and military aircraft, enabling operational advantages such as increased range, loiter time, and offload capabilities. When integrated with projected 2030 engine technology, this advanced aircraft configuration is expected to provide at least 60 percent mission fuel burn reduction compared to current day technology"
Notes: Deliverables
  A robust framework that's versatile to integrate any number of disciplines
  Communicate seamlessly with different analysis tools
  Predicts an optima or a set of optima which are better than baseline design
Problem Definition
  Theoretical structure for the seamless interfacing of different solvers/analysis tools
  Test it by actual implementation

## Slide 6: Tightly Coupled Integrated Systems
Propulsion
Controls
Structures
AeroD
Notes: Deliverables
  A robust framework that's versatile to integrate any number of disciplines
  Communicate seamlessly with different analysis tools
  Predicts an optima or a set of optima which are better than baseline design
Problem Definition
  Theoretical structure for the seamless interfacing of different solvers/analysis tools
  Test it by actual implementation

## Slide 7: Relevance of a Framework
Notes: Deliverables
  A robust framework that's versatile to integrate any number of disciplines
  Communicate seamlessly with different analysis tools
  Predicts an optima or a set of optima which are better than baseline design
Problem Definition
  Theoretical structure for the seamless interfacing of different solvers/analysis tools
  Test it by actual implementation

## Slide 8: Features of the Framework
Solver Agnostic
  Simple plug and run with any solver
  Treat analysis tools as black boxes
Modularity
  Integrate additional disciplines without modification
  Building on top of each other
Simplicity
  User need not work with more than 2 files at most
Scalability & Flexibility
  Scaling to thousands of design variables should be feasible
Efficient Gradient Evaluation
  Offer different methods to compute gradients efficiently
Goals of this Project
Leverage OpenMDAO* [1]
Notes: Solver Agnostic
  Simple plug and run capability for any analysis tools with very minimal changes to the framework
  Treats analysis tools as a black box
Modularity
  Integrate additional disciplines without modifying other discipline structure
  Building on top of each other
Simplicity
  User need not work with more than at most 2 files
Scalability & Flexibility
  Scaling to thousands of design variables should be feasible
Efficient Gradient Evaluation
  Offer different methods to compute gradients efficiently

## Slide 9: Design of the Framework

## Slide 10: Three Key Modules of the Framework
Note:
Arrows do not indicate flow of information or order of processes carried out
Notes: For four key tasks are identified
1. Optimization
2. User interface
3. Outflow Processor – Responsible for processing and managing all the analysis
4. Inflow Processor – Responsible for evaluating and fetching all the design variables, obj functions, constraints

## Slide 11: Interface
User inputs to define the setup
Only 1 or 2 files at max. to tweak
Structure is similar to Optimization packages in Python/MATLAB
Check for consistency and errors
Notes: Module Manager: Receives the input as vectors, the design variables are classified on the basis of their disciplines and sent to the discipline module. Module manager is the primary tool that inputs as well as outputs the necessary information from OpenMDAO to the discipline manager.

## Slide 12: OpenMDAO + Discipline Manager
Notes: Module Manager: Receives the input as vectors, the design variables are classified on the basis of their disciplines and sent to the discipline module. Module manager is the primary tool that inputs as well as outputs the necessary information from OpenMDAO to the discipline manager.

## Slide 13: Framework Building - I

## Slide 14: Framework for 2D ASO
Some of the methods used here are directly inspired from Sachit Vekaria’s work on “Multi-disciplinary Design Optimization for Aerodynamic Efficiency and RCSR” under the guidance of Professor Avijit Chatterjee, Professor Bharat Adsul and Professor Hemandra Arya.

## Slide 15: Common Parameters
Parameters | Methods/Values
Optimization Algorithms | SLSQP
Tolerance | 10E-6
Gradients | Finite Differencing
Mesh Strategy | Remesh the entire domain
Geometry Parameterization | Bump Function

## Slide 16: Benchmarking with SU2 Test Case
Parameters | Values
Mach no. | 0.8
AoA | 1.25deg
Flow | Inviscid
Solver | Euler
Problem Setup | 
Obj Fn | Min. Cd
DV | 20 shape amplitudes
Constraints | None

## Slide 17: Benchmarking with SU2 Test Case
Results​ | 
Baseline Cd​ | 209.95​
Optimized Euler​ | 4.39​
Optimized Test Case​ | 4.5​
Optimized RANS​ | 27.47​

## Slide 18: Results – 2D | Constrained Optimization
Constrained Problem
M = 0.8
AOA = 1.25 degrees
Function | OpenMDAO Optimized
Cd | 0.0025126 (88%)
Cl | 0.4
Problem Setup | 
Obj Fn | Min. Cd
DV | 20 shape amplitudes
Constraints | Cl*>0.4 A*/A > 0.85

## Slide 19: Benchmarking with ADODG Test Case-1
Parameters | Values
Mach no. | 0.85
AoA | 0 deg
Flow | Inviscid
Solver | Euler
Problem Setup | 
Obj Fn | Min. Cd
DV | 20 shape amplitudes
Constraints | Thickness > Baseline's

## Slide 20: Benchmarking with ADODG Test Case-1

## Slide 21: RCS + CFD
Obj Fn | Min. Cd
DV | 20 shape amplitudes
Constraints | A*/A >1 RCS*/RCS < 0.7
Cd baseline | 92
Cd optimized | 84
Cd optimized Vinh | 71
Parameters | Values
Mach no. | 0.8
AoA | 1.25deg
Flow | Inviscid
CFD Solver | Euler
CEM Solver | MLFMM*
*Multi-Level Fast Multipole Method

## Slide 22: RCS + CFD

## Slide 23: Framework for 3D ASO

## Slide 24: Challenges
Adhoc constraint implementation to prevent wiggly designs
Finite Differencing is very time consuming
  1 CFD ~ 5 mins
  20 DV ~ 100 mins for 1 gradient calculation
  100 function evaluations ~ 10,000 mins!
  Adjoint based derivative ~ <5 mins for 1 gradient evaluation
Meshing strategy – Remesh entire volume
  1 million ~ 2-3 mins
  100 function evaluation ~ 200-300 mins
  Mesh deformation ~ 4-5 seconds
Previous framework was not SCALABLE to 3D ASO problems

## Slide 25: Revamping the Framework for 3D ASO with MDO Lab Tools
Pygeo
ADflow
IdWarp
Optimizer

## Slide 26: MDO Lab Tools
Notes: Module Manager: Receives the input as vectors, the design variables are classified on the basis of their disciplines and sent to the discipline module. Module manager is the primary tool that inputs as well as outputs the necessary information from OpenMDAO to the discipline manager.

## Slide 27: Framework Testing | Case1
Parameters | Values
Mach no. | 0.85
AoA | 0 deg
Flow | Inviscid
Solver | Euler

## Slide 28: Result | Case-1

## Slide 29: Result | Case-1

## Slide 30: Framework Testing | Case2
Parameters | Values
Mach no. | 0.85
AoA | 2.79 deg
Flow | Turbulent – 20 Million Re
Solver | RANS
Cd reduction | 49%

## Slide 31: Framework Testing | Case2

## Slide 32: Framework Testing | Case 3
Parameters | Values
Mach no. | 0.839
AoA | 3.06 deg
Flow | Turbulent – 11 Million Re
Solver | RANS
DV | 144 shape + 6 twist

## Slide 33: Framework Testing | Case 3

## Slide 34: Framework Testing | Case 3

## Slide 36: Framework Testing | Case 3

## Slide 37: Conclusion and Future Work
Created a MDO framework
Specifically vetted for 2D and 3D ASO problems
It is generalizable to incorporate other disciplines
RCS module is still in process

## Slide 38: Results – 2D | FEKO Benchmarking | Cylinder
EMCC Benchmarks

## Slide 39: Results – 2D | FEKO Benchmarking | Airfoil